## Slide 1: Floorplanning
Workshop Session 4

## Slide 2
Synthesis
Floorplanning/Power Network
Placement
CTS
Routing
RC Extraction
GDS Generation
Physical Verification
Yosys, OpenSTA
init_fp, ioplacer, pdn
RePLace,OpenDP
TritonCTS
FastRoute, TritonRoute
SPEF-Extractor
Magic
Magic
Open-source EDA Tools
Input
Input
Input
Input
Input
Input
Input
Input
Output
Output
Output
Output
Output
Output
Output
Design.v, Design.sdc, Std_cells.lef, Std_cells.lib
Design_gate_level_netlist.v
Design_gate_level_netlist.v, macro.lef, macro.cfg
Floorplan.def
Floorplan.def
Placement.def
Design_gate_level_netlist.v, Placement.def
CTS.def, CTS_netlist.v
CTS.def
Routing.def
Routing.def
Design.spef
Routing.def
Design.gds, Design.lef
Design.gds
Input
Output
APR Step
EDA Tool

## Slide 3: Contents
Floorplanning
  Row Formation
    Number of Rows
    Height of Rows
Core Utilization
Aspect Ratio
Power Distribution Network
  Power Connections
LAB PRACTICE

## Slide 4: Floorplanning
What is Floorplanning?
  Defining the area of the chip
    Die area
    Core area
    Formation of rows
    Height of rows
Metaphorically speaking,
  Acquiring the land/plot to build the house

## Slide 5
CORE AREA
IO PAD AREA
IO PAD AREA
IO PAD AREA
IO PAD AREA
Die Area
IO pad Area + Core Area
IO pads where pins are connected
Core Area where logic bocks are placed
Die Area vs Core Area

## Slide 6: Row Formation
Formation of rows is carried out after deciding the area
Why Rows?
How are the rows decided?

## Slide 7: Row Formation
For the above formula to work both the parameters must be constant.
  Core area height is constant [ as discussed earlier ]
  Standard Cell Height?
    There are a large number of cells [AND, OR, NOT, NOR, flops, etc. ]
      Who’s height to use in the formula?
The height of every standard cell is the same
  In Skywater 130 nm, the height is 2.72 um

## Slide 8: Core Utilization
CORE AREA
IO PAD AREA
IO PAD AREA
IO PAD AREA
IO PAD AREA
MUX
NAND
NOR
FF
AND
NOT
8
MUX
NAND
NOR
FF
AND
NOT
Standard Cells
Core Area
Core Area with 100 % Utilization
Core Area with less than100 % Utilization

## Slide 9: Aspect Ratio
Aspect Ratio = 1
Aspect Ratio = 0.5
Aspect Ratio = 2

## Slide 10: Power Distribution Network
PDN distributes the power from the external source to the internal standard cells.
The aim is to provide power to the standard cells without the voltage drop
The process starts with inserting metal rails along the rows

## Slide 12
We start by placing the metal rows
Note that each layer is either power or ground
Power
Power
Power
Ground
Ground
Ground

## Slide 13
Power
Ground
Vertical straps are then inserted
Power and ground are separated and they don’t overlap
Power
Power
Ground
Ground
offset
pitch
Pitch: The center to center between 2 adjacent straps
Offset: The distance from the edge of the core to the first metal layer

## Slide 14
Power
Ground
Power
Power
Ground
Ground
The complete power grid but without power ring
Horizontal straps are then inserted
Power and ground are separated and they don’t overlap

## Slide 15
The complete power grid with power rings

## Slide 16: Conclusion
The area and number of rows are fixed at the floorplan step
Core utilization and aspect ratio are used when the die area is not defined
Power distribution network follows:
  Metal rails
  Vertical Strips
  Horizontal Strips
  Power Ring