## Slide 1: Clock Tree Synthesis
Workshop Session 6

## Slide 2
Synthesis
Floorplanning/Power Network
Placement
CTS
Routing
RC Extraction
GDS Generation
Physical Verification
Yosys, OpenSTA
init_fp, ioplacer, pdn
RePLace,OpenDP
TritonCTS
FastRoute, TritonRoute
SPEF-Extractor
Magic
Magic
Open-source EDA Tools
Input
Input
Input
Input
Input
Input
Input
Input
Output
Output
Output
Output
Output
Output
Output
Design.v, Design.sdc, Std_cells.lef, Std_cells.lib
Design_gate_level_netlist.v
Design_gate_level_netlist.v, macro.lef, macro.cfg
Floorplan.def
Floorplan.def
Placement.def
Design_gate_level_netlist.v, Placement.def
CTS.def, CTS_netlist.v
CTS.def
Routing.def
Routing.def
Design.spef
Routing.def
Design.gds, Design.lef
Design.gds
Input
Output
APR Step
EDA Tool

## Slide 3: Contents
Clock Tree Synthesis
Why Clock Tree Synthesis?
  Timing
  Power
  Signal integrity
Solution
  Tree
    H-Tree
    Grid [ Mesh Tree ]
    Spine Tree

## Slide 4: Clock Tree Synthesis
Clock Tree Synthesis (CTS) is a process which distributes the clock evenly to all sequential elements in a design
It adds buffers and inverters to achieve zero/minimum skew or balanced skew

## Slide 5: Clock Tree Synthesis
Why can’t the clock be routed like any other net?
Implications on clock
  Timing
  Power
  Signal integrity etc.
CORE AREA
IO PAD AREA
IO PAD AREA
IO PAD AREA
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
Clock
FF

## Slide 6: Timing
Skew
  Clock skew is the difference in the arrival time of a clock signal at two different Flops.
Jitter
  Clock jitter is the deviation of a clock edge from its ideal position in time
Slew
  Transition time of the clock- rise/fall time of the clock
Insertion Delay
  The amount of time taken by the clock signal to travel from source to sinks is called the insertion delay

## Slide 7: Skew
ff2
q2
ff1
q1
clk
Combinational logic
Launch Clock
Capture Clock
2ns
3ns
Launch clock
Capture clock
Skew
= 3-2 =>1 ns
Positive skew

## Slide 8: Skew
ff2
q2
ff1
q1
clk
Combinational logic
Launch Clock
Capture Clock
2ns
3ns
Launch clock
Capture clock
Skew
= 2-3 => -1 ns
Negative skew

## Slide 9: Jitter
Ideal clock
Realistic clock
Jitter
CAUSES
PLL Noise
Power Supply Ripples
Temperature Variations
Crosstalk Between Signals
50ns
50ns
100ns
150ns

## Slide 10: Slew
10 %
10 %
90 %
90 %
Time taken from 10% till 90% during the transition

## Slide 11: Insertion Delay
The time from the source of the clock to the sink is called insertion delay
CORE AREA
IO PAD AREA
IO PAD AREA
IO PAD AREA
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
FF
Clock
FF
Source

## Slide 12: Power
The clock capacitance consists of
  Clock Generation [PLL etc]
  Clock Elements [Buffers etc]
  Clock Wires
  Clock Load Of Sequential Elements
The clock networks are so huge that they require a large percentage of the total chip power.

## Slide 13: Signal Integrity
Noise can disrupt the clock
  Irregular clock edges can effect the register operation
Slow clock transition
  Bad
Fast clock transition
  Power
  Area

## Slide 14: Solution?
Trees
  H-Tree
  Mesh Tree [ Grid]
  Spine tree

## Slide 15
Clock Tree
Try to make a tree
  Balance the RC-Delay
Challenges ?
  Excessive power usage
  Large RC for each net
  Signal integrity at risk
Solution ?
  Buffered Tree

## Slide 16
Good slew rates
Less total switching capacitance
Lower RC Values
Buffered Tree

## Slide 17: H-Tree
Advantages
  The skew in this type of tree is lower
  Power consumption is tolerable
Disadvantages
  Very low floorplan flexibility
H-Tree

## Slide 18: Grid
Advantages
  Skew is determined by the grid density and not overly sensitive to load position
  Signals are available across the chip
  Extreme low skew values
Disadvantages
  Power hungry
    Large wire cap
    Large routing area
FF
FF
FF
FF
FF
FF
FF
FF
FF

## Slide 19: Spine Tree
Advantages
  Small RC delay
  Floorplan flexibility higher than H-Tree, But lower than Mesh Tree
  Consumes less power as compared to Mesh Tree/Grid
Disadvantages
  Difficult to balance delays, high skew
FF
FF
FF
FF
FF
FF
FF
FF

## Slide 20: A Quick Comparison
Structure | Skew | Cap/area/power | Floorplan Flexibility
H-Tree | Low /medium | Low | Low
Grid | Low | High | High
Spine | High | Medium | Medium