## Slide 1: Routing and Checkers
Workshop Session 7,8

## Slide 2
Synthesis
Floorplanning/Power Network
Placement
CTS
Routing
RC Extraction
GDS Generation
Physical Verification
Yosys, OpenSTA
init_fp, ioplacer, pdn
RePLace,OpenDP
TritonCTS
FastRoute, TritonRoute
SPEF-Extractor
Magic
Magic
Open-source EDA Tools
Input
Input
Input
Input
Input
Input
Input
Input
Output
Output
Output
Output
Output
Output
Output
Design.v, Design.sdc, Std_cells.lef, Std_cells.lib
Design_gate_level_netlist.v
Design_gate_level_netlist.v, macro.lef, macro.cfg
Floorplan.def
Floorplan.def
Placement.def
Design_gate_level_netlist.v, Placement.def
CTS.def, CTS_netlist.v
CTS.def
Routing.def
Routing.def
Design.spef
Routing.def
Design.gds, Design.lef
Design.gds
Input
Output
APR Step
EDA Tool

## Slide 3: Contents
What is Routing
Global Routing
Detailed Routing
Filler Insertion
Design Rule Check (DRC)
Layout Vs. Schematic (LVS)

## Slide 4: What is Routing
Routing is the stage after the CTS where,
  Interconnects are established by determining precise paths for each nets
  This includes interconnections of the standard cells, macro pins and I/O pads of the chip
  Tool knows the exact location of the standard cells, macros and IO pads
  Metal layers are used to create the electrical connections to complete the connectivity as defined in the net list
Routing in OpenLANE is a two stage process;
  Global routing - fastroute
  Detailed Routing- tritonroute

## Slide 5: Remember this ?
Interconnects are implemented using available metal layers in sky130nm technology.

## Slide 6: Routing
Metal layers are placed on top of each other in alternating directions.
This avoids the capacitive effect to arise between parallel metal plates.

## Slide 7: Routing
ff2
ff1
Q1
Launch Flop
Capture Flop
ff2
ff1
Q1
Din1
Din2
Dout1
Dout2
Clk
Let's Consider this example,
D2
D2

## Slide 8: Routing
Global Routing
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
Din1
Din2
Dout1
Dout2
1
2
2
ff2
ff1
ff2
1
ff1
Rough routing guides are established
Outlines for actual route
Not actual routing

## Slide 9: Why global routing?
Analyze congestions
Identifies available paths
Minimizes detouring

## Slide 10: Routing
Detailed Routing
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
Din1
Din2
Dout1
Dout2
1
2
2
ff2
ff1
ff2
1
ff1
Actual interconnects established
Least detoured path considered
Multiple iterations are performed to overcome Design Rule Violations

## Slide 11: Maze Routing - LEE’s Algorithm
A commonly used Algorithm,
Path between two points is found and connection established
The idea is to create a path between Source and Target of two cells,
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
Cell1 S
1
2
3
4
3
5
4
6
5
7
6
2
3
4
5
2
3
3
Cell 2
T
5
4
4
6
4
5
6
7
6
5
4
5
5
4
5
6
7
8
5
6
6
6
7
6
7
7
7
7
7
5
6
6

## Slide 12: LEE’s Algorithm
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
Cell1 S
1
2
3
4
3
5
4
6
5
7
6
2
3
4
5
2
3
3
Path 1
Path 2
Cell 2
T
5
4
4
6
4
5
6
7
6
5
4
5
5
4
5
6
7
8
5
6
6
6
7
6
7
7
7
7
7
5
6
6
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
Cell1 S
1
2
3
4
3
5
4
6
5
7
6
2
3
4
5
2
3
3
Cell 2
T
5
4
4
6
4
5
6
7
6
5
4
5
5
4
5
6
7
8
5
6
6
6
7
6
7
7
7
7
7
5
6
6

## Slide 13: Filler Cell Insertion
Gaps in between the standard cells in the rows and rail discontinuity, results in DRC violations.
Filler cells are usually added which are physical cells containing n-well, p-well and power rails.
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
Din1
Din2
Dout1
Dout2
1
2
2
ff2
ff1
ff2
1
ff1

## Slide 14: Before and After Filler cell Insertion
N-Well mask before filler insertion
N-Well mask after filler insertion

## Slide 15
Sign Off
Checks to ensure that,
  Final layout implements all design rules
  Identify any unmatched nets that may occur due to short/open circuits.
  Layout Vs Schematic (LVS) identifies any differences in the nets.

## Slide 16: Design Rule Check (DRC)
DRC is based on the technology file provided along with the PDK.
Magic is used for Design Rules Checking.
Let’s take this example to understand DRC!

## Slide 17: DRC
So after routing certain design rules are checked to ensure seamless routing.
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
Din2
Din1
Dout1
Dout2
1
2
2
ff2
ff1
ff2
1
ff1

## Slide 18: Some common DRC rules
Remember what you see on the mask is what you see on the silicon!
t1
t2
1. Wire width
t1
t2
2. Wire Spacing

## Slide 19: DRC
Next set of common DRC’s occur when,
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
I/O PAD AREA
Din2
Din1
Dout1
Dout2
1
2
2
ff2
ff1
ff2
1
ff1

## Slide 20: DRC Violation
DRC violation type: Signal Short
Solution: Use different metal layers

## Slide 21: Some common DRC rules
1. Via width
2. Via Spacing

## Slide 22: Layout Vs. Schematic
Netgen is used for Layout Vs Schematic LVS check.
Two step process:
  Extraction: The process extracts the devices and their connectivity from the physical layout, and then generates a netlist interpretation of the layout to be used in the comparison step.
  Comparison: The process compares the extracted netlist to the schematic netlist, and reports all discrepancies, which must then be debugged and resolved.
Extracted SPICE by Magic vs. Verilog netlist

## Slide 23: Key Things To Remember
Metal 4 and 5 are usually used for power routing, i.e. for the power grid.
Routing violations must be avoided.
The design needs to be DRC and LVS clean.
This can be achieved by tweaking and tuning design parameters in the flow.